## Slide 1: Overview of ground-based part of the PsA research project and PWING
PsA research project and PWING project

## Slide 2: Phase 4 8 EMCCD ASIs of PsA + PWING
Tromsø: 100 Hz EMCCD ASI - BG3 (inoperative now) Monochromatic ASI（10 Hz） x 2 （427.8 nm + 844.6 nm）→ currently 20 Hz 20 Hz Fluxgate magnetometer 5 channel photometer
Sodankyla: 100 Hz EMCCD ASI – BG3 Many supporting instruments of SGO
Tjautjas: 100 Hz EMCCD ASI – BG3
Kevo: 100 Hz EMCCD ASI – BG3（PWING）
Gakona in Alaska: 100 Hz EMCCD ASI – BG3（PWING）
Poker Flat in Alaska: 100 Hz EMCCD ASI – BG3（PWING）
MLAT 65
MLAT 60
Tromsø
Sodankyla
Kevo
Tjautjas
← Alaska (Gakona, Poker Flat)

## Slide 3: A few things about the data
Quick Look data browser: https://ergsc.isee.nagoya-u.ac.jp/psa-gnd/bin/psa.cgi
Digital data in raw format: https://ergsc.isee.nagoya-u.ac.jp/psa-gnd/pub/raw/ Password is required for access IDL code for reading/plotting the data is provided
Conjunction Interval Finder (CIF): https://ergsc.isee.nagoya-u.ac.jp/psa-gnd/bin/cif.cgi

## Slide 4: https://ergsc.isee.nagoya-u.ac.jp/psa-gnd/bin/psa.cgi
Tromsø
100 Hz
Sodankyla
100 Hz
Tromsø
844.6 nm
Tjautjas
100 Hz
Tromsø
427.8 nm
Kevo
100 Hz
Gakona
100 Hz
Poker Flat
100 Hz
Quick Look Data Browser

## Slide 5: https://ergsc.isee.nagoya-u.ac.jp/psa-gnd/bin/cif.cgi
Conjunction Interval Finder
New!

## Slide 6: https://ergsc.isee.nagoya-u.ac.jp/mw/index.php/CampaignObs/Campaign2017
List of Good
Conjunctions

## Slide 7: Long-term prediction of conjunction

## Slide 8: Rocket experiment in Dec 2020
NASA Rocket launch is scheduled in Dec 2020 Launch site: Poker Flat, Alaska Launch window: Mid December
An EMCCD camera and an sCMOS camera are planned to be installed in the down-range of rocket trajectory from the Japanese team
High-energy electron detector, auroral cameras and magnetometer will be on-board by the effort of Japanese team